## Slide 1: Hera AFC Data decoding procedure
Jean-Baptiste Vincent,
DLR Institute for Planetary Research, Berlin, Germany

## Slide 2: Relevant documents
Data | Document title | File name
EDDS Raw | Hera Data Delivery Interface Control Document | ESA-HERA-OPSOPH-IF-22002, i1r2 20240429 (DDID).pdf
ECSS Header | Telemetry and telecommand packet utilization | ECSS-E-70-41A30Jan2003.pdf
SCOS-2000 general | SCOS-2000 Database Import ICD | egos-mcs-s2k-icd-0001-version7.2-FINAL.pdf
SCOS-2000 Hera | Hera SCOS-2000 database | *.dat files
AFC Data Header | AFC User Manual | HERA-JOP-AFC-UM-30001_05_AFC_User_Manual.pdf
AFC Data Packet | FaintStar2 datasheet | FS_CM_WO_17_002_D8_FS2_Datasheet_ICD.pdf
Note: the info in these documents is unfortunately not always 100% up to date.
The database itself is likely to be the most reliable source of information.

## Slide 3: EDDS Raw
One string of hexadecimal characters (0-9, a-f, A-F)
Each pair of characters represent one Byte
First Byte is always “00”
Then for each packet:
  First 2 characters (1 Byte) are a packet counter
  Next 8 characters (4 Bytes) are the Length of the packet in characters
  Next L characters (L/2) Bytes are the packet data

## Slide 4: EDDS Raw example
00
00
0000003C
091ac0020017208b0300010000000030230531ca0101000000000000d459
01
0000003C
091ac0020017208b0300010000000030230531ca0101000000000000d459
02
00000150
091ac00700a1208b03000200000000303e058ff7011804610000068204620000010004630000090000f000000020042000000001042100000100042200000900042300000010042400000fff00e20000000100e300000001046700000fad0468000003ff00e50000003004aa0000000204ab0000000200ee000000ff00ef000000ff046d00000fac010f0000000200e20000000200400000004200ac00000008046600000241520d
03
…
Always Zero
Packet #0, 60 characters (0x3C)
Packet #1, 60 characters (0x3C)
Packet #2, 336 characters (0x150)

## Slide 5: Packet Data
SCOS-2000 Header (6 bytes) | Packet Data Common Header (variable size) | AFC Packet header + data (variable size) | Packet Trailer (1 byte)
Common for all instruments
Contains similar info for all instruments, but depends on packet type
Defined by instrument manufacturer
Error Correction Code, EndOfPacket, …
The byte structure of the Packet Data Common Header can be found in the database, but only if you know certain identifiers that must be extracted from the packet itself…

## Slide 6: Example: AFC Navigation Image